## Slide 1: UART
Universal Asynchronous Receiver/Transmitter

## Slide 2: Serial & Parallel Communication

## Slide 3: Serial Communication
Only ONE data bit is sent every clock cycle.
EXAMPLES:
UART, USART, I2C, PCI-E, RS-232, USB.
Tx
Rx
control
control
Data line

## Slide 4: Parallel Communication
Multiple data bits are sent every clock cycle.
EXAMPLES:
Conventional PCI, IEEE-1284, Parallel ATA.
Tx
Rx
control
control
Data lines

## Slide 5: Serial Vs Parallel. why is serial more popular?
 | Serial Communication | Parallel Communication
Bit/Cycle | Only one bit per cycle | Multiple bits per cycle
Speed | Slow | Fast
Hardware size | Small | Large
Disadvantages |  | Speed is affected due to clock skew. Cable length is limited due to Crosstalk.

## Slide 6: Communication Circuit Types
Tx
Rx
Tx/Rx
Rx/Tx
Tx
Rx
Rx
Tx
Simplex
Half Duplex
Full Duplex

## Slide 7: Synchronous and Asynchronous
An asynchronous protocol has no common clock line that regulates data transmission speed.
Users must set both devices to communicate at the same speed.
The receiver performs oversampling to indicate when the data is suitable to capture.
A synchronous protocol has a common clock line that regulates data transmission speed.
The receiver captures data at either the rising or falling edge of the clock.

## Slide 8: Oversampling
Oversampling is the technique used by the receiver to capture the input transmitted input bit.
Used asynchronous communication.
Instead of capturing the data once at the rising edge of a common clock.
It captures at the middle of the transmitted bit.
Sampling rate a commonly 16 or 8.
A sampling rate of N means that the receiver clock frequency must be N times that of the transmitter
Transmitter clock

## Slide 9: Baud Rate
Baud rate is the number of serial bits per second that can be transmitted/received over a certain communication line.
It is a measure of the speed of the system.
A baud rate of9600, is 9.6kbps(9600bps) in a serial system.
An 8-bit parallel system with 9600 baud transmits 9600x8 bits per second(9600kBps).
This transmitter requires a clock of 9.6kHz.
Common Baud Rates(bps) | 
2400 | 38.4k
4800 | 57.6k
9600 | 76.8k
14.4k | 115.2k
19.2k | 230.4k
28.8k | 250k

## Slide 10: Baud Rate Generation
Typically there is no crystal oscillators that has the frequency required to the transmitter or receiver.
A typical way is to use a frequency divider, this can be implemented using a counter.
A 4-bit mod-16 counter divides the clock by a maximum of 16.
How to find the proper counter?

## Slide 11: Error checking: Parity Bit
A parity bit is a basic method to check whether the received data is correct or erroneous.
It can be either even parity or odd parity.
With even parity, the bit is only 0 when the number of ones is even.
With odd parity, the bit is only 0 when the number of ones is odd.

## Slide 12: The UART Circuit

## Slide 13: UART
UART stands for Universal Asynchronous Receiver/Transmitter.
A serial data transmission interface.
NOT a protocol or a standard.
A circuit found in microcontrollers or stand-alone IC’s.

## Slide 14: UART Frame
When idle, the transmitter send a stream of ones.
The start bit is 0.
The data length can either be 5, 6, 7, 8, or 9.
The parity bit is optional and can either be odd or even.
The stop bit/s can be 1, 1.5, or 2.

## Slide 15: UART Operation: Transmitter

## Slide 16: UART Operation: Receiver

## Slide 17: Basic Transmitter Architecture

## Slide 18: Commercial UART Architecture
Source: opentitan.org

## Slide 19: Questions?!.....Maybe